## Slide 1
TankMaster Introduction

## Slide 2: Lesson Goals
Get basic knowledge about the TankMaster Software
  What is TankMaster?
  How does TankMaster work?
  Which operations are available?
  How to install TankMaster

## Slide 3: What is Tank Master?
TankMaster is
  Developed by Rosemount Tank Radar
  Specially developed to get the most out of an automatic tank gauging system
  A configuration software
    Installation/configuration of Rosemount field equipment
  A tank inventory management software including
    Inventory calculations
    Batch handling
    Report handling
    Alarm handling
    History sampling
  Open communication interface
    That easily connect to other HOSTS/DCS

## Slide 4: TankMaster - A Unique Software
100% in-house developed
Windows platform
All languages...
  Can easily be translated
OPC Server
  Easy integration to other systems
Easy site customization
  Visual Basic

## Slide 5: TankMaster - Programs
Administrator program
  Administrator
User interface programs
  WinOpi
  WinSetup
  WinView
  TankMaster.net
System / Additional programs
  Editor
  TankServer
  Master and Slave Servers

## Slide 6: TankMaster - Administrator
Administrator program
  ”Task Manager” for TankMaster
  Autostarts when PC is started (default setting)
  Autostart of TankMaster programs at PC reboot
  Status of TankMaster servers
  View File info (e.g. version)
  Backup function
    Important to do when configuration is done
  Restore function
    Restor of backup

## Slide 7: TankMaster - WinSetup
Graphical user interface for installation, configuration & service of Rosemount field equipment
  Protocols
    Enable protocols
    Configure slave servers
    COM port settings
  Install/Configure field devices
    FCU
    Tank hub
    5900, 5300, 5400
    Rex, Pro, TRL2
    DAUs
  Install tanks
    Connect field devices
    Configure input parameters
    Type of tank/strapping table
    System unit
Notes: WinSetup
  Graphical user interface for installation, configuration and service of Saab field equipment
Protocols
  Enable protocols
  Configuring slave servers
  COM Port settings
Install/Configure field devices
  FCU
  REX/ Pro/ TRL/2
  DAUs
  IO Terminals
Install tanks
  Connect field devices
  Configure input parameters
  Type of tank/Strapping table
  System unit

## Slide 8: TankMaster WinOpi
Operator user interface
  Tank inventory management
    Realtime inventory calculations
    According to API standard
  Tank Groups
    Product/Area
  Product Table
    Easy volume calculation setup/tank
  Alarms
    Management
    Level/Volume/Flow/Leak alarms
  Trends
  Reports
  Batch management

## Slide 9: TankMaster WinView
WinView is a new cost effective version of WinOPI.
  For smaller depots where full inventory calculation support is not needed
  Excellent entry level to TM
  Use the same WinSetup as WinOpi (no changes in WinSetup).
  Is an option in the HW key.
Included functions:
  Alarms
  Host comunication (option in HW key)
  Reports (log report) etc.
Excluded functions:
  Batchfunction
  Redundancy
  Custody Transfer etc.
Notes: TankMaster WinView is a software package with basic inventory capabilities. It is a cost efficient alternative for operational control at smaller tank terminals, marketing terminals, biofuels and chemical plants etc. Configuration is made with WinSetup, which is included in the delivery.

## Slide 10: TankMaster.net & Editor
TankMaster.net
  Note! Separate software
  Creates a webpage presenting live data from connected Tank Master systems
  Only internet explorer needed
  View inventory data
  View historical data
  Make reports
Editor
  Translate TankMaster
  Special rebuild of windows and views

## Slide 11: TankServer
TankServer
  Core program in TankMaster
  Collecting data from Master servers
  Performs all inventory calculations
  Handles all alarms
  External hosts can connect to TankServer using OPC
Master Servers
  Collecting data from field devices and provides data to tankserver
    Modbus Master – rosemount Equipment
    IOT Master – I/O Terminals
    Enraf GPU Master – Enraf CIU / gauges
Slave Servers

## Slide 12: Master Servers & Slave Servers
Master Servers
  Collecting data from field devices and provides data to tankserver
    Modbus Master – rosemount Equipment
    IOT Master – I/O Terminals
    Enraf GPU Master – Enraf CIU / gauges
Slave Servers
  Provides data to DCS / HOST systems
    Modbus Slave
    ASCIILT Slave
    Data Highway Plus Slave

## Slide 13: Program modules
PC Server Side
PC Client Side

## Slide 14: Network Connection
TankMaster runs on Standard Windows network in Local Area Network (LAN) and Wide Area Network (WAN)
  Connection to HOST/DCS system
  Inventory Data public via TankMaster.net
  Several WinOpi clients to same tankserver
TANK SERVER
TANK SERVER
CLIENT
CLIENT
CLIENT
Ethernet
DCS
TM.Net
W W W
www.tankmaster.net
TANK SERVER
WAN
CLIENT
LAN
Notes: TankMaster runs on Standard Windows network in Local Area Network (LAN) and Wide Area Network (WAN)
  Connection to HOST/DCS system
  Inventory Data public via TankMaster.Net
  Several WinOpi clients to same tankserver

## Slide 15: Network handling
All functions that can be performed locally can also be done to remote sites
  WinSetup
    Installation of tanks
    Installation and configuration of devices
    Setup protocols
    View real-time communication log
  WinOpi
    Display Tank Inventory information
    Alarm handling
  Connection of several servers at the same time

## Slide 16: TankMaster - In a Network
Slave
Servers
Server Side
Client Side
WinSetup
WinOPI
Server PC
Client PC
LAN - Ethernet
WinSetup
WinOPI
Modbus Master
Master Servers
External Device
Slave Device
DCS, HOST
Server Side
Client Side
Tank Server

## Slide 17: TM - Protection Levels
Administrator
  Default password: admin
  Network configuration
  User accounts
Supervisor
  Default password: super
  Configuration of system, protocols, devices and tanks
  Tools, Closing WinOpi, Creating Alarm Groups
Operator
  Default password: oper
  Entry functions, creating groups, accepting alarms
Wiew Only
  Default password: view

## Slide 18: TM - Protection Levels
User Manager
  Manage user account
  Add/remove user accounts
  Change user level
Protection Level
  Possible to set access level
    Accepting alarms
    Report handling
    All windows in TankMaster
Possible to lock PC to only run WinOpi
  WinOpi always run maximized
  Not possible to change ot any other program
Audit Log
  Log all actions done by operator logged in
Notes: TA BORT!?!?!?

## Slide 19: TM Redundant System
A redundant system gives
  High availability
  No work stop
  No data loss
Redundancy for:
  Inventory calculations
  Alarm handling
  Batch handling

## Slide 20: TM Redundancy Normal operation
WinOpi clients are always connected to primary server
  Auto detect Primary/Backup
  Tankserver and Batchserver
Data is replicated from primary to backup
  Only configure devices on one PC
  Installation of new devices and tanks is possible
Tankservers work in ”Hot Redundancy”
  Both servers are polling data from FCU
  Online data from field is polled from both servers

## Slide 21: Complete Redundant System
Vital parts exist in pair
  If one part fails the other takes over automatically
  ”hot redundancy”
Switch Redundancy
TankMaster redundancy
  Inventory calculations
  Alarms
ModbusMaster redundancy
  Comports/FBM
  2140/FCU communication
FCU 2160/2165/2175 redundancy (optional)
2410 redundancy
  Field communication
  Fieldbus redundancy
5900 redundancy

## Slide 22: TankMaster Hardware Key
Key only required in TM Server
No driver needed
Different types of keys
  WinOpi: Silver with black text
  WinView: Silver with blue text
  WinSetup: Silver with green text
  Service (48h): Red with black text
  Service (unlimited time): Silver with red text
  TM.Net: Yellow with black text
Old TankMaster keys. Works on version 6.A1 build 14 and older
New TankMaster keys. Works on version 6.A1 build 15 and later

## Slide 23: Tank Master Requirements
TM-04-0060 ”TankMaster minimum Requirements
  PC requirements for TankMaster 4.G0 or higher
    Hard drive: 40 GB (TM needs approx. 500 MB)
    Two RS-232 ports (USB can be used instead)
    One parallell port or USB for TM hardware key
    Graphical card: 1152*864, 65536 colors
    Hardware key: One key for each PC with a TM server or client
  Hardware TankMaster Network PC
    Known brand PC – 2 GHz, 2048 MB RAM (up to 20 tanks: 1024 MB)
  Hardware TankMaster Standalone or Client PC
    Known brand PC – 1 GHz, 1024 MB RAM (up to 20 tanks: 512 MB)
  Operatin system, 4.H1 and earlier
    Windows XP SP2
    Windows 2003 Server
  Operating systems, 5.B0 and higher
    Windows Vista, SP1
    Windows XP, SP2 & SP3

## Slide 24: TankMaster Installation
Starts installation of TankMaster
Installs field device ini file package
Installs acrobat reader, needed for reading user’s guide

## Slide 25: TankMaster Installation
Install Demo
  Possible to run WinOpi without hardware dongle
  Good to use for practice of all functions in WinOpi
  Demo for customer
Program Files and User Gui
  Install ’sharp’ version of TM
Software modules being installed
  WinOpi
  WinSetup
  TankServer
  Master/Slave Protocol Servers
Installation requires reboot of PC

## Slide 26: TankMaster Demo
If Demo installed
  TM Demo database needed to be installed afterwards
  Will install 6 tanks which is preconfigured with volume/density calculations
Level will automatically go up and down
Test
  Alarm handling
  Batch handling
  Reports
  Historical data
  More...

## Slide 27: TankMaster Demo
Switching betweed demo and real mode
  Done by using two reg files
  Found on TM installation CD under \Enable Function
  To enable DEMO click Demo_Enable
  To disable DEMO click unreg Demo_Disable